Dipartimento di Scienze E Scienza dell’informazione / Corso di Laurea in: Ingegneria Informatica
Autonomous Quadcopter Flight / with PX4 and ROS2
Thesis type: Experimental
Studente: / Massimo Girardelli	Relatore: / Prof./Dott. Luigi Palopoli
ACADEMIC YEAR 2019/2020 / Abstract / This thesis is the design and development of a software application for the control of quadcopters and other flying drones. / Quadcopters have gained more attention in the past years due to their versatility and potential in various fields, including surveillance, aerial photography, and environmental monitoring. / Although ready to use solutions and similar open source projects exist, an easily configurable, with a graphical interface and indoor capabilities that responds to external inputs doesn’t and this project aims to provide a working template that can be customized for different applications. / Controls can be sent by the GUI by people or via ROS2 messages / The end goal of the project is a proof of concept of all the different components working together, the ROS interface allows seamingless integration with many other devices in the robotic world. / This drone is capable of indoor flying with position provided by external beacons

Sommario
Elenco delle Tabelle
Elenco delle Figure
Acronyms, Abbreviations and important terms

PX4	PX4 is the Professional Autopilot. Developed by world-class developers from industry and academia, and supported by an active world wide community, it powers all kinds of vehicles from racing and cargo drones through to ground vehicles and submersibles.
ROS2	obot Operating System version 2, middleware that enables fast and easy messages communications between different nodes on a network
NED	orth-East-Down coordinate system where the X-axis is pointing towards the true North, the Y-axis is pointing East and the Z-axis is pointing Down, completing the right-hand rule.
FRD	ront-Right-Dwon coordinate system where the X-axis is pointing towards the Front of the vehicle, the Y-axis is pointing Right and the Z-axis is pointing Down, completing the right-hand rule.
SITL	Software in the Loop, a simulation tool that reproduces the flight controller behavior
LTS	“Long Term Support”, an LTS version of software recives supports for many years to come and thus is more preferred for compatibility
GUI	Graphical User Interface
OptiTrack	Motion capture system, used to detect the drone position with a tracker
Commander	Main computer from where the drone is controlled
Companion	Single board computer mounted on the drone

Introduction and aim of the thesis
The aim of this thesis is to provide a system that allows drones to fly with the support of external position detection systems, in this case with Optitrack, Motion Capture Systems, ROS2, Pixhack flight controller and Rockchip ROCk 4 C+ board.
This thesis also provides an easily employable simulation environment to test the different flight options preseted by the commander

Thesis organization
The structure of the thesis is shown in the following list:
• Hardware employed pros, cons and limitations
• Software employed introduction: description of the system used and all the software for this project
• Deployment: steps to take to deploy a system like this
• Simulation results: the proposed algorithms are tested through a SITL simulation, with the Gazebo simulator.
Demo
• Flying results results: flight performance, obstacle, battery life,
Chapter I
Hardware:
This is the list of components used and some reasons behind the choices that were made
- Holybro X500 V2 Development Kit
  Main frame of the drone, it’s a good all-in-one solution for a quadcopter, it mounts 4 920 Kv motors, perfect for this application, lower Kv motors offer more torque and less fan speed, which is desired in this application give the weight of the whole system, a higher Kv motor would strugle more.
  The Pixhawk 6C flight controller offers the right connectivity that we need for this esoteric application and easily provides the CPU and RAM taht we need.
- 5000 mAh Li-Po batteries
A massive 5000 mAh Li-Po battery powers the motors, the flight controller	and the companion computer.
The 4S configuration offers 14.8V, when charged it can reach 16.8V, the	drone will strugle to lift below 14V.
The exact model used is: “Dinogy Ultra Graphene 4S 5000mAh 80C”
- ROCK 4 C+ (Companion)
  A single board computer, similar to a Raspberry PI but with a 64-bit architecture.
  It’s a hexacore ARM processor with 4GB of LPDDR4 RAM, which is plenty for our needs.
  The GPIO PINS are used for serial communication with the flight controller
  Connection is done with Wifi and a SSH shell and power is delivered via USB
- Commander computer
  Any computer that can run the commander programs, it’s possible to use the Companion itself but there are no guarantees of recovering the system in case of disconnection.
- OptiTrack
  3D Motion Capture Systems mounted in the laboratory, the precision is <1 cm, latency is around 30ms, publish rate is 360Hz by default but the drone remains stable up to 50 Hz of data recieved in case of network congestion.
  The 9 cameras placed around the flying area, provide an accurate position estimation. The position is sent through the network and must be decoded by a client.
Chapter II
Software:
In this software chapter I will explain the systems and tools used to bring this project to life and the inner workings of the components to kae the drone fly.
System tools:
Ubuntu 22
This was a very important decision since every distribution of Ubuntu has	it’s own ROS2 distribution and the latest LTS (for now) only supports	Ubuntu 22
ROS2 Humble
Middleware used to share all messages between applications and to launch most of the applications, ROS resolves around Nodes, Topics and Messages:
- Nodes: a process interfacing with the ROS libraries, different nodes can run on different machines while being connected through networking and be visible to each other.
- Topics: a pipe-like virtual structure within ROS that can be used to share messages between different nodes, it can be interfaced as a publisher or as a subscriber, each topic routes one specific message type.
- Messages: data structures that travel through the nodes, it is not system-dependent and provides primitive types like booleans, integers, floats, arrays and nested messages types.
  Custom messages were built for this projec

The optimal QoS (Quality of service) options were used:
- Best effort, to reduce network congestion, most messages are ephemeral and gets overriden a few milliseconds later
- Transient local: the publisher is responsible for delivering the last message tho subscribers who joined after it was published
- Keep last: only keeps the last message, previous values are invalid anyway
The humble distrubution was used as it was the LTS version supported	at the moment of developing the project
Python 3.10.12
Python was used for the ease of developement and speed of deployment	as it doesn’t need compilation; python with PX4 has also much more	documentation and examples than any other language.
Other programming languages that have better performance like c++	were considered but discarted due to minimal documentation, much more	devloping time and a very slow overall deploment experience and	unpleasant experience:
- ROS2 compilations have massive overheads, even for well written cmake files while python has none;
- a part of the code runs on the companion computer that, while powerful, is not really suited for continuous compilations
  (installing all the PX4 dependencies and building the optitrack package took more that 1 hour and a half)
The runtime overhead of python gets completly eclipsed by the network	delay.
The version 3.10.12 is the offically supported by ROS2 Humble

PX4
Open source flight control solution for drones.
ROS is used by PX4 to provide an offboard control functionality, with a linux companion computer. In this way its possible to control the PX4 flight stack using a software outside of the autopilot. PX4 supports both versions of the robotic operating system, but while the communication between ROS 2 and the autopilot is done through a ROS2-PX4 bridge (MicroXRCEAgent).
There are 2 ways to connect and read messages: ROS2-PX4 bridge or	MavLink
MavLik has a sligh different notation and needs it own libraries and	messages while the ROS2-PX4 bridge only requires sourcing the	message (done automatically when sourcing the whole ROS enviroment).
The custom PX4 messages are used by most of the software used.

This list contains the 3 macro components used (Companion, Commander and Tracking) and software to launch to the whole system:

Companion
The role of the companion is to run the MicroXRCEAgent service, the command to run is:
sudo MicroXRCEAgent serial --dev /dev/ttyS2 -b 921600
The client starts a ROS2 node that published topics with informations	like current position, velocity, status, and subscribes to other topics to	recieve commands, tracked position and keep-alive signals.
Communication with the flight controller is done on the serial port ttyS2	with a baud rate of 921600 to transmit all the data.

Figure 1: Flight controller on the left and companion pc on the right

For this particulat usecase a custom firmware was build to access particular informations like land detection, battery status.
1. Commander
  The commander computer is responsible for running the following processes:
px4-py.py
the main controller of the system, sends heartbeat signals to the companion to keep it alive, recives updates on position, velocity, status etc. from the companion, recieves data from the GUI, and most importantly elaborates all the data and messages to produce an action to send to the drone.
This process is based on callbacks when a new message is detected, the main class OffboardControl(Node) keeps a record of the lates recieved.
If there is no GUI (set in config.py), it procedes with the selected mode in the configuration file, otherwise it listens for action messages.
Some actions are simply redirected to the companion (like arm, disarm, shutdown), other action that continue over time start a thread that compute and published mesasges to the companion over time and is stopped if a different a different command is sent.
This this design the main thread constantly updates his own varables based on the lates message published by the companion, while every action over time is his own thread that based on the current status of the drone and can be stopped in any moment.

- Gui.py
  This graphical interface is a quality of life tool that considerably speeds up testing and validation since it makes possible to interface (in a human mode) with the controller, enabling runtime changes to the operating mode without editing and restarting the whole system.

  Figure 2: gui.py
  It has many functionalities and offers all the relevant information on screen:
  - ARM arms the drone if the above contitions are met
  - DISARM disarms the drone before it takes off or when it landed, does not work mid flight
  - TAKEOFF takes of to the height declared in src/config.py by the variable takeoff_height
  - LAND lands at (0,0) local frame, position cannot be overriden, this is a limitation of the offboard mode because it would require a different mode to land normally on locaton, disconnecting from the commander
  - STOP stops any activity and hold the position
  - TEST button to test features, currently lands on a random position
  - KILL emergency stop, terminates the flight immediately and stops the propellers, even mid air
    USE WITH CAUTION
  - SPIN spin on self with omega = spin speed slider
  - ROUTINE starts hovering in circle around (0,0), at height = height , omega = omega slider,radius = radius
  - GOTO goes to position x,y,z in NED frame (CAUTION WITH Z COORDINATES)
  - PATH load a path file like src/medium.json and the drone fill follow all points with speed = moviment speed slider
  - UPDOWN goes up and lands, mainly for testing
  - NONE default, no activity, the drone will hover
  - GRAPH shows arudimentary graph of position offset between the set position and the current position, gives a rough estimate of the offset
    other commands and tabs are self explanatory

This program is independent and the whole system can work without this piece of software since it doesn’t comunicate directly with the companion but only to the commander, this is a design choice to improve compatibility and automation.
Every information is accessible with the command line or a program with a ROS interface and every action is replicable with a script

Tracking
The tracking component is needed for indoor flight and is expected by	default, GPS flight need a change in the parameters of the flight controller
A previously mentioned the tracking system used for this project is the	OptiTrack as it offers a sub-centimeter precision when correctly	calibrated, but any other tracking device can be used as long as it can	publish ROS pose messages
The software needed to run the tracking system are:

Motive
The proprietary software that is physically attached to the	cameras, it published multicast messages int he network, must be	configured with the shape of the tracker used.
Must be interfaced witha client to acecs the date published.
- optitrack_interface
  Figure 3: Motive software
  python nat net client, it decodes the OptiTrack messages and publishes geometry_msgs.PoseStamped, a standard ROS message that can be accessed from the other programs
- opti-to-px4.py
  python program listens to the OptiTrack messages and converts geometry_msgs.PoseStamped to VehicleOdometry messages, a PX4 message type and throttles the output to s stable 100Hz

WHY?
Why doing all these conversion of messages?
Let’s procede with steps: the first conversion from Motive to	optitrack_interface is need because Motive is a general pourpose trackign	system and publishes it’s own format and not designed to work out of the	with ROS so this step is unavoidable.
But in the second part from optitrack_interface to PX4 we convert ROS	message to ROS message, can’t we just skip the middle part and do	Motive-PX4?
The answer is yes, but not always.
Let me explain, this setup was done in an existing laboratory and a	standard PoseStamped is recognized by any ROS program and is the	most suitable for the data transferred, so an existing setup might alerady	have this system setup.
There might be also the case of multiple objects detected or multiple	drones, opti-to-px4 only relays the messages with a give ID to the drone
In any case I developed an all in one solution for a direct Motive-PX4 and	it’s called opti-to-px4-v2.py

This is all the software that is used to make the drone fly which is either proprietary software, forked and modified code or developed from scratch by me, all details are in the main repository.
More programs are used in the simulation section.

Chapter II
Software:

## Offboard control
Offboard control is employed to perform each of the tasks shown in this thesis, this means that the vehicle responds to position velocity or attitude setpoints computed by algorithms running on a companion computer, while the PX4 autopilot is charged only with actuating such commands and stabilizing the drone. PX4 offboard mode has some requirements that must be satisfied in order to be ran, as detailed in :
• At least a stream of > 2 Hz of setpoints commands that shall be sent to the autopilot from the companion computer.
• At least one of the following pose/attitude information has to be available (GPS, optical flow, visual-inertial odometry, mocap, etc.)
• The vehicle must be previously armed, and it must receive an appropriate stream of commands prior to the offboard mode engagement.
• RC communication must be disabled. If an RC command is issued to the autopilot or the stream of setpoints commands is stopped, then the vehicle will exit the offboard mode and enter a failsafe state, thus landing.
• Offboard mode requires also a continuos connection to a remote MAVLink system or a ground control station software (such as QGroundControl), otherwise if such connection is lost the vehicle will enter a failsafe mode and land.

## Simulation Tools
Simulation tools are used to control a vehicle model via ROS 2/PX4 code. This is done trough Software in the Loop (SITL) in which the flight stack runs on computer as opposed to Hardware in the Loop (HITL) simulation in which the firmware runs on a controller board.
 The PX4 autopilot supports a variety of simulators:
• Gazebo
• FlightGear
 • JSBSim 24 2.4 – Simulation Tools
 • JMAVSim
• AirSim Gazebo is the simulator used in this thesis project as it directly support a ROS integration and it comes pre-installed with the ROS 2 package.

Gazebo
Gazebo is an open source 3D simulator, it can be used to simulate autonomous robots and in particular is suitable to test computer vision related algorithms. Moreover it is necessary to point out that it supports also multi-vehicle simulation [26]. The simulator supports a lot of vehicle models, the one used for the thesis project has been the Iris quadrotor which comes as part of the PX4 autopilot SITL section. Such models are defined in the .sdf4 format through which is possible to easily modify the starting model and implementing custom plugins such as sensors. While it is still possible to be used independently, the Gazebo simulator comes preinstalled when installing a ROS distribution via the set of packages called gazebo_ros_pkgs. Because of that and due to the fact that extensive documentation is provided by the autopilot docs, the gazebo simulator has been employed for the SITL simulation in this thesis work.
UAV model
The PX4 SITL package provides a UAV model of the 3DR Iris, which is a commercially available multicopter.
While it is possible to start with the base model offered via the PX4 Autopilot to simulate the most simple tasks (i.e. takeoff, reach a target) through Gazebo. In order to test the more complex tasks, which require the usage of additional sensors (i.e. camera), it has been necessary to modify the sdf model in order to add sensors plugins:
• Camera: a ventral camera is added with the libgazebo_ros_camera plugin, the camera points downward and is used both for image collection and to detect the position of the apriltag used during the precision landing procedure.
• Ultra-wide band sensor: Similarly, the ultra wide band sensor is added via a specific plugin (libros2_px4_gazebo_uwb).
• Laser scan/Laser altimeter sensor: In order to simulate the operations of a laser altimeter a libgazebo_ros_ray_sensor plugin is employed. This plugin is not specific to a laser altimeter and so it is necessary to specify a narrow angle in the .sdf file. This plugins offers an array of different methods regarding the output message type of the data, this is done by modifying the entry in the .sdf file. In this thesis work two of them has been employed: – sensor_msgs/LaserScan message type: employed in the control section of this thesis whenever the altitude of the UAV had to be published as feedback, in order to provide a 2D scan with multiple results. – sensor_msgs/Range message type: employed in the estimation section of the code, this message type returns a single distance value which is the minimum of all ray ranges recorded by the sensors
World model
The PX4 Autopilot SITL package provides the user with a convenient bash file in which is possible to instruct the world and model files employed during the simulation, the bash file is the sitl_multiple_run.sh. With this is possible to simulate multiple vehicles using the Gazebo simulator. The file has been suitably modified in order to employ the mars terrain world file and placing a platform simulating the UGV on top of which the precision landing is performed.

Due to this, it is necessary to convert any position data coming from the simulation environment towards the algorithms paired with the autopilot, one example is the ground-truth measurement coming from the libgazebo_ros_p3d and employed during the estimation algorithm validation and tuning.
Drone status topic
All the nodes composing the control section of the drone are subscribed to a custom topic called the status topic, defined by the Status.msg

Each server then has the information regarding which action is being executed, if any. Furthermore, if any goal request is made while the drone is completing a previously received goal the action server will reject the goal request.
Goal rejection
In order to avoid a goal interfering with each other it is necessary to reject a goal request if another task is still in execution. This is done through the knowledge of the drone status topic (section 3.1.2). This algorithm component is executed in the goal_callback which is included in all action servers, the action is employed to demonstrate this simple procedure, implemented in the callback function:
This procedure, while shared by all action servers, is slightly different in the case of the takeoff action server due to the fact that the takeoff action is not necessary in case the UAV is in hover mode. In this specific case the takeoff request will be rejected if the drone is already hovering. In every pseudo code displayed in the following sections this procedure will be substituted by the phrase If the goal request is valid ... in order to avoid repeating the same pseudo-code in every section.
Goal cancellation
Each action server has the capability of canceling the previously sent goal, even if accepted by the action server. This can be done either through the dedicated abort service or through pressing the CTRL+C key on the keyboard while on the client window of the terminal. Once the goal request has been sent to the server the drone starts to move toward the target requested by the action server, if a cancellation is sent (trough a suitable callback) then the UAV sets back the hover mode via the control node.
Communication with the PX4 autopilot
Each action server has the possibility of communicating with the PX4 Autopilot by publishing the required trajectory setpoints, as already seen in section 2.3.2 the input to the low level controller can be either a position or a velocity array. In this thesis work case the position setpoint has been employed for the simpler tasks, like the takeoff or reaching a given target while the velocity setpoints have been used when requiring either a trajectory tracking capability or more control in general. The topic used to communicate to those controllers is TrajectorySetpoint_PubSubTopic while the PX4 odometry (VehicleOdometry_PubSubTopic) has been used as feedback for each action server except the precision landing one (see chapter 4 for details).
Chapter III
Offboard algorithms:
Algorithms
 organization In order to provide the UAV with the capabilities necessary to perform the tasks, from the simpler ones i.e. takeoff to the more complex i.e. taking images following a precise pattern and performing a precision landing, a number of algorithms have been developed. Furthermore by taking advantage of the different types of interfaces made available by the robotic operating system it has been chosen to organize such algorithms mainly through ROS 2 actions. The main tasks performed by the UAV in the simulation are:
• Takeoff
• Reaching a user-defined target
• Orbiting around a specific target while taking images
• Providing a coverage of a designated area while performing a grid sweep
• Precision landing To do so, an action server has been developed and associated to each task. Subsequently an action client, has been set up, in order for the user to request the tasks to be performed, thus creating a request/reply communication model between the action clients and server. Everyone of these server is then started via a single launch file for ease of use, and are paired with a continuously running control node. The organization is while the code organization is examined more in depth in the appendix A. Each of the main launch files starts some nodes and processes, described below:
• Simulation launch file:
The gazebo_sitl_multiple_run.sh is a bash script used to start: ∗ Launch the Gazebo simulation environment ∗ Generate the world model for the martian ground ∗ Position the drone model, which is a modified Iris model, in the Gazebo simulation
• Configuration file:

PID Controller
PID controller introduction
In order to provide the autopilot offboard controller, which responds to a given trajectory setpoints input, an external PID controller is employed. This controllers computes the velocity input to be transmitted to the autopilot instead of sending directly the position request in order to have a smoother transition towards the target. The controller is employed in the get images, area coverage and land on spot algorithms as a trajectory tracking controller. The PID controller is employed because, even if it doesn’t guarantee optimal control or control stability is broadly applicable and does not rely on the knowledge of the model . As shown in a previous section (section 2.3.2) the autopilot flight stack provides with a position and attitude controllers which can be used to stabilize the drone. Instead, the proposed customizable high-level controller is used to compute the best velocity setpoints in the trajectory tracking section of each action server in which is employed.
PID controller architecture
A PID (Proportional integral derivative) controller is a mechanism which employs sensor feedback which is widely used. From the feedback the error value e(t) is computed, which is the difference of the actual measured process variable y(t) from the reference setpoint r(t), the correction input u(t) is applied computed from the PID terms. In this thesis case the feedback may come from the already available PX4 Odometry messages, which then are compared to the reference position to be reached by the drone. Instead, in the precision landing case the error is computed directly through the relative position of the UAV with respect to the rover . In this thesis case the control input u(t) are the velocity setpoints [vx, vy, vz] sent to the autopilot flight stack, the interaction of the PID controller
PX4 and ROS 2 for offboard control
ROS is used by PX4 to provide an offboard control functionality, with a linux companion
computer. In this way its possible to control the PX4 flight stack using a software outside
of the autopilot.
PX4 supports both versions of the robotic operating system, but while the communication
between ROS 2 and the autopilot is done through the ROS2-PX4 bridge (Figure
A.2.3) the communication with the first version can be done either via two bridges (the
PX4-ROS2 bridge and subsequently ros_bridge) or through a MAVROS package over
MAVLink protocol.
The usage of the second version of ROS is highly recommended, by the development
team of PX4, as the PX4-ROS2 bridge is able to take advantage of the communication
middleware (DDS/RTPS).

In this thesis the second version of ROS has been employed thus requiring only to setup
the connection to the autopilot through the PX4-ROS2 bridge.
From the communication standpoint the PX4 autopilot employs an RTPS protocol and
a DDS middleware in order to interface itself with an offboard DDS application (such as
ROS 2 nodes), in this way it is possible to exchange uORB2 topics sent by the client (the
PX4 autopilot) to RTPS messages to the agent side (offboard computer) and vice versa.
The connection between such devices is enabled trough an UART or UDP link. This
translation and communication bridge is called the microRTPS bridge, the main components
of such architecture are shown in figure
In both cases the packages are populated at build time via the mentioned python scrips
contained in the PX4 firmware. Since not all uORB topics are made available to the ROS
application as a default setting if specific messages are required to be transmitted from
uORB to ROS messages then these scripts must be ran manually.
Both packages are available as GitHub repositories for ease of access an installation.
In order to perform it, is’s necessary to clone the repositories and then run the build
command, as shown in the installation tutorial Appendix-A.
The packages are placed on the agent side of the communication, in the ROS 2 workspace
directory.

Offboard control
Offboard control is employed to perform each of the tasks shown in this thesis, this means
that the vehicle responds to position velocity or attitude setpoints computed by algorithms
running on a companion computer, while the PX4 autopilot is charged only with actuating
such commands and stabilizing the drone.
PX4 offboard mode has some requirements that must be satisfied in order to be ran, as
detailed in [22]:
• At least a stream of > 2 Hz of setpoints commands that shall be sent to the autopilot
from the companion computer.
• At least one of the following pose/attitude information has to be available (GPS,
optical flow, visual-inertial odometry, mocap, etc.)
• The vehicle must be previously armed, and it must receive an appropriate stream of
commands prior to the offboard mode engagement.
• RC communication must be disabled. If an RC command is issued to the autopilot

the stream of setpoints commands is stopped, then the vehicle will exit the offboard
mode and enter a failsafe state, thus landing.
• Offboard mode requires also a continuos connection to a remote MAVLink system
or a ground control station software (such as QGroundControl), otherwise if such
connection is lost the vehicle will enter a failsafe mode and land.

Chapter IV
Algorithms organization
In order to provide the UAV with the capabilities necessary to perform the tasks, from the
simpler ones i.e. takeoff to the more complex i.e. taking images following a precise pattern
and performing a precision landing, a number of algorithms have been developed.
Furthermore by taking advantage of the different types of interfaces made available
by the robotic operating system it has been chosen to organize such algorithms mainly
through ROS 2 actions.
The main tasks performed by the UAV in the simulation are:
• Takeoff
• Reaching a user-defined target
• Orbiting around a specific target while taking images
• Providing a coverage of a designated area while performing a grid sweep
• Precision landing
To do so, an action server has been developed and associated to each task. Subsequently
an action client, has been set up, in order for the user to request the tasks to be performed,
thus creating a request/reply communication model between the action clients and server.
Everyone of these server is then started via a single launch file for ease of use, and are
paired with a continuously running control node. The organization is displayed in figure
3.1 while the code organization is examined more in depth in the appendix A.
Each of the main launch files starts some nodes and processes, described below:
• Simulation launch file
– The gazebo_sitl_multiple_run.sh is a bash script used to start:
* Launch the Gazebo simulation environment
* Generate the world model for the martian ground
* Position the drone model, which is a modified Iris model, in the Gazebo
simulation

Conclusioni
Inserire qui il testo delle conclusioni.
Bibliografia
Bianchi, G., Verdi, G. & Rossi, M., 2018. Titolo dell'articolo. Journal Name, 48(3), pp. 11-15.
Rossi, M., Bianchi, G. & Verdi, G., 2018. Titolo dell'articolo. Journal Name, pp. 10-15.
Verdi, G., 2017. Titolo del capitolo. In: R. Cristiano, a cura di Titolo del libro. Ancona: CasaEditrice, pp. 10-20.

ISTRUZIONI PER L’USO DEL MODELLO

Salvare due copie di questo documento, la prima da conservare come modello, la seconda da utilizzare per il proprio elaborato curricolare.

Parametri di riferimento del presente documento

Margini del documento: sinistro 3 cm; destro 3 cm; rilegatura 0,5 cm; superiore 3 cm; inferiore 3,5 cm

Numeri di pagina: in basso a destra (frontespizio e dedica non sono numerate)

Principali stili adottati
la raccolta di stili completa è visibile cliccando su Stili

Stili di paragrafo (il testo)
Normale: da usare per il corpo del testo; carattere Times New Roman; corpo 11 pt; interlinea 1,5; rientro prima riga 0,5 cm; nessuna spaziatura prima e dopo; giustificato
Citazione: da usare per le citazioni lunghe (almeno 4-5 righe); carattere come il corpo del testo; corpo 11 pt; interlinea singola; rientro prima riga assente; rientro a sinistra e a destra 0,5 cm; spaziatura prima 6 pt, dopo 12 pt; giustificato
Abbreviazioni: da usare per le sigle e le abbreviazioni nella tavola iniziale; carattere come il corpo del testo; corpo 11 pt; interlinea 1,5; prima riga sporgente di 2 cm; spaziatura dopo 6 pt; giustificato; mantieni assieme le righe

Stili di paragrafo (i titoli)
Titolo 1: da usare per i titoli delle parti principali del testo (tavola delle sigle, introduzione, capitoli, conclusioni, bibliografia, indice); carattere come il corpo del testo; corpo 16 pt; interlinea singola; rientro prima riga assente; spaziatura dopo 96 pt; allineamento centrato; anteponi interruzione (affinché il titolo cominci con l’inizio di una pagina)
Titolo 2: da usare per i titoli dei paragrafi; carattere come il corpo del testo; corpo 12 pt; grassetto; interlinea singola; prima riga sporgente di 0,5 cm; spaziatura prima 24 pt, dopo 12 pt; allineamento a sinistra; mantieni con il successivo; mantieni assieme le righe
Titolo 3: da usare per i titoli dei sottoparagrafi; carattere come il corpo del testo; corpo 12 pt; corsivo; interlinea singola; prima riga sporgente di 0,5 cm; spaziatura prima 12 pt, dopo 12 pt; allineamento a sinistra; mantieni con il successivo; mantieni assieme le righe
Titolo 4: da usare per i titoli dei sotto-sottoparagrafi; carattere come il corpo del testo; corpo 12 pt; tondo; interlinea singola; prima riga sporgente di 0,5 cm; spaziatura prima 12 pt, dopo 6 pt; allineamento a sinistra; mantieni con il successivo; mantieni assieme le righe
NB: I titoli dei capitoli, dei paragrafi e dei sottoparagrafi sono numerati automaticamente in modo strutturato (1, 1.1, 1.1.1). La numerazione dei capitoli prevede la dicitura automatica “Capitolo 1”, “Capitolo 2”, ecc. Nella tavola delle sigle, introduzione, conclusioni, bibliografia, indice la numerazione è stata eliminata

Stili di carattere
Enfasi (corsivo): da usare per la parola o le parole in corsivo
Enfasi (grassetto): da usare per la parola o le parole in grassetto
Enfasi (maiuscoletto): da usare per la parola o le parole in maiuscoletto
Sigla corsivo: da usare per le sigle in corsivo come ad es. ccl
Sigla tondo: da usare per le sigle in tondo come ad es. dh
NB: Gli stili di carattere consentono un maggiore controllo del testo e lo rendono più stabile. Per rimuovere uno stile di carattere o una formattazione applicata a una o più parole il comando a tastiera è: CTRL+barra spaziatrice oppure CTRL+MAIUSC+Z

Bibliografia
La lista dei riferimenti bibliografici alla fine del documento è generata con il comando Riferimenti > Bibliografia > Inserisci bibliografia. È possibile aggiornare la lista dalla voce di menu contestuale (pulsante destro mouse) Aggiorna campo.

Lista delle tabelle
La lista delle tabelle è generata con il comando Riferimenti > Inserisci indice delle figure. Nella finestra di dialogo selezionare Etichetta didascalia: Tabella. È possibile aggiornare la lista dalla voce di menu contestuale (pulsante destro mouse) Aggiorna campo.

Lista delle figure
La lista delle figure è generata con il comando Riferimenti > Inserisci indice delle figure. Nella finestra di dialogo selezionare Etichetta didascalia: Figura. È possibile aggiornare la lista dalla voce di menu contestuale (pulsante destro mouse) Aggiorna campo.

Sommario
Il sommario è generato con il comando Riferimenti > Sommario > Sommario personalizzato. Nella finestra di dialogo selezionare Formati: Da modello. È possibile aggiornare la lista dalla voce di menu contestuale (pulsante destro mouse) Aggiorna campo.
SI RICORDI DI ELIMINARE LA VOCE “SOMMARIO” DAL SOMMARIO.